## Slide 1: Risk Management – Asbestos Removal
Hazard 2 – Asbestos

## Slide 2: Risk Management – Asbestos
Heat stress management procedure has been developed to o provide guidelines and information for the discovery, handling and removal of materials suspected or known to contain asbestos and the safe working procedures to be adopted to prevent and minimise the risk of releasing airborne respirable asbestos fibres during these activities.

## Slide 3: Roles and Responsibilities
Employer/QSE Manager will:
  Conduct risk assessment and prepare plans;
  Ensure staff have been provided with appropriate training for the work activity;
  Prepare and Asbestos Control Plan for licenced removal work;
  Prequalify subcontractors to carry out removal work when required;
  Make notifications to the regulator when applicable;
  Ensure staff have received health assessments for conduct of removal work where required under legislation.
  Develop site specific emergency procedures to manage potential emergencies associated with exposure to ACM.

## Slide 4: Roles and Responsibilities
Project Manager/ supervisor is responsible for:
  Obtaining the Asbestos Register for the site or commission a competent person to investigate to identify potential ACM;
  Ensuring an Asbestos Control Plan has been prepared for licenced work and a SWMS for all other work involving asbestos;
  Ensure the notification made to the regulator is on site if applicable
  Ensure an Asbestos Removal Supervisor is readily available or present when the licenced work is being carried out;
  Limiting access to the work area and ensuring the barricades and signs are in place;
  Implement controls that are consistent with the hierarchy of control and ensuring appropriate procedures are followed according to legislation.

## Slide 5: Roles and Responsibilities
Workers must:
  Not conduct any work involving asbestos without first having the appropriate training;
  Follow workplace procedures to ensure compliance with legislation is maintained;
  Complete tracking certificates correctly;
  Wear the RPE you have been fit tested for with a clean-shaven face

## Slide 6: Licencing Requirements
WHS Regulation 458 requires a PCBU who commissions the removal of asbestos at the workplace to ensure the asbestos removal work is carried out by a licensed asbestos removalist who is appropriately licensed to carry out the work, unless specified in the WHS Regulations that a licence is not required.
There are two types of licences: Class A and Class B. The type of licence required will depend on the type and quantity of asbestos or ACM that is being removed at a workplace

## Slide 7: Licencing Requirements
Type of Licence | 
Class A | Can remove any amount or quantity of asbestos or ACM, including: Any amount of friable asbestos or ACM Any amount of ACD Any amount of non-friable asbestos or ACM
Class B | Can remove: Any amount of non-friable asbestos or ACM (Note: A Class B licence is required for removal of more than 10m² of non-friable asbestos or ACM but the licence holder can also remove ACD associated with removal of up to 10m² of non-friable asbestos or ACM) ACD associated with the removal of non-friable asbestos or ACM. (Note: A Class B licence is required for the removal of ACD associated with the removal of more than 10m² of non-friable asbestos or ACM but the licence holder can also remove ACD associated with removal of up to 10m² of non-friable asbestos or ACM)
No Licence Required | Can remove: Up to 10 m² of non-friable asbestos or ACM ACD that is: Associated with the removal of less than 10 m² of non-friable asbestos or ACM Not associated with the removal of friable or non-friable asbestos and is only a minor contamination.

## Slide 8: Hazard Identification & Assessment
An asbestos removalist should consider not only the direct hazards that are associated with the asbestos removal work but also those hazards related to the work activity and the work environment (for example, demolition or construction)

## Slide 9: Hazard Identification & Assessment
Confined spaces
  Removing asbestos in a confined space should only be undertaken where it is not possible to avoid doing work in that space. A safe system of work should be developed for inclusion in the management plan or removal control plan.
Falls
  Work at heights should not be undertaken the work can be performed on the ground, if asbestos removal work must be undertaken at height, the WHS Regulations apply.
Heat Stress
  Heat related hazards can be created by the restrictions imposed on the workers while wearing asbestos removal PPE. Control measures could include:
    Selection of appropriate PPE fitted to reduce the build-up of heat
    Cool cotton underclothing
    Scheduling of appropriate work breaks
    Job rotation
    Cool drinks readily available
    Providing shade where possible
    Education of workers regarding heat stress risks and controls.

## Slide 10: Hazard Identification & Assessment
Electrical equipment
  When undertaking asbestos removal work, the risk associated with electrical equipment should be controlled.
  Electrical equipment in the work area should be removed or de-energised.
    De-energised equipment must be secured to prevent inadvertent re-energising.
  All portable electrical equipment, including flexible leads should comply with AS/NZS 3012:2003 Electrical installations-construction and demolition sites

## Slide 11: Control Measures - Warning Signs
Signs and barricades must be used to clearly indicate the area where the asbestos removal work is being performed.
Must be placed in positions so that people are aware of where the asbestos removal work area is and should remain in place until removal is completed and clearance to reoccupy the space has been granted.
These signs should be weatherproof, constructed of lightweight material and adequately secured so they remain in prominent locations.
Signs should be in accordance with AS 1319-1994 Safety signs for the occupational environment for size, illumination, location and maintenance.

## Slide 12: Control Measures – Barricades
The use of barricades assists with traffic control and prevents access to the removal site and removal work area.
The purpose of barricades is to delineate and isolate the asbestos removal area with appropriately placed barricades.
Barricades can take various forms, from tape to solid hoarding.
The location of barricades will depend on the physical environment and the level of risk.
An assessment of the removal site should determine the appropriate placement of barricades.

## Slide 13: Control Measures – Tools & Equipment
Tools and equipment that can be used during asbestos removal work that have been designed to capture or suppress dust or are used in a way that is designed to capture or suppress respirable dust.
The following equipment may be required on site before the work begins:
  Disposable cleaning rags
  Bucket of water and/or misting spray bottle
  Sealant
  Warning signs and/or barrier tape.
  Asbestos warning signs and barricades
  Wet saw
  Water

## Slide 14: Control Measures – Prohibited Tools & Equipment
Tools and equipment that generate dust must not be used on asbestos. These include:
  High speed abrasive power and pneumatic tools, for example angle grinders, sanders, saws and high speed drills
  Brooms and brushes (unless brushes are used for sealing)
  High pressure water spray
  Compressed air

## Slide 15: Control Measures - PPE
All workers will be provided with suitable PPE for asbestos removal work.
Workers must use the PPE given to them by the asbestos removalist.
PPE must be worn at all times during the work in the removal area.
PPE includes clothing e.g., coveralls, gloves & safety footwear, and Respiratory Protective Equipment.
The appropriate level of PPE is determined by risk assessment and is recorded in the Asbestos Removal Control Plan for the project

## Slide 16: Control Measures - Decontamination
Decontamination for the work area, workers, PPE & tools
  Eliminates and minimises exposure to airborne asbestos fibres, particularly to persons outside the asbestos removal work area.
Contaminated items must not be removed unless they have been decontaminated or contained.
If an item is not able to be decontaminated, or is not suitable for decontamination, it should be placed in a sealed container and disposed of in accordance with the WHS Regulations.
The sealed container must be decontaminated before it is removed from the asbestos removal work area.

## Slide 17: Training & Certification
Certification
  Workers (including asbestos removal supervisors) who are carrying out licensed asbestos removal work are required to acquire a certification by completing units of competencies to show they have the relevant training to be able to remove asbestos.
  The units of competency completed by the person will determine what type of asbestos work they can carry out.

## Slide 18: Training & Certification
Training
  A licensed asbestos removalist must provide appropriate training to a worker carrying out licensed asbestos removal work at the workplace to ensure the work is carried out in accordance with the asbestos removal control plan for the workplace.
  This additional training to the general training that is provided on the identification and safe handling of asbestos and the appropriate controls referred to in the Code of Practice: How to Safely Remove Asbestos.
  A worker who is carrying out licensed removal work must receive training that is designed specifically for the workplace where work is being or is to be carried out.
  This training should occur before the commencement of each asbestos removal job.
  The training should include:
    The nature of the hazards and risks
    How asbestos affects a person’s health
    The risk of exposure to airborne asbestos
    The control measures in place for the maintenance of the asbestos removal control plan for the job
    The methods and equipment that will be used to do the job properly
    Choosing, using and caring for PPE RPE
    Decontamination procedures
    Waste disposal procedures
    Emergency procedures
    Any other legal requirements (for example, contaminated sites)

## Slide 19: Monitoring & Review
Monitoring
  Asbestos removal work will be monitored to ensure the procedure is working effectively and that appropriate records are being kept.
Review
  A review of the currency of this procedure will be conducted if there are any changes in legislation or advances in current work practices or equipment. A system review will be conducted not less than eery three years
Auditing
  An internal audit will be conducted on the implementation and adherence to this procedure by the QSE Manager not less than annually.
  It may also be audited during scheduled surveillance audits conducted by a third party as part of the maintenance of Certification to ISO 14001, AS 4801, ISO 9001 and inclusion on the Federal Safety Commissioners list of accredited builders.
  Audit outcomes are used to develop corrective actions which may result in changes to this procedure

## Slide 20: Record Keeping
Training records
  Records of all training must be kept while the worker is carrying out the work and for five years after the day the worker stops carry out the work.
  These records must also be available for inspection by the regulator
Asbestos Removal Control Plan
  All persons involved with the work activity must review the plan and sign to say they understand the procedures and they agree to follow them as outlined.
  The plan must be kept on site for the duration of the project.

## Slide 21: Legislation & Other Requirements
Work health and Safety Act 2011
Work Health and Safety Regulation 2011 (Qld)
How to safely remove asbestos code of practice 2011
AS/NZS 1716 Respiratory Protective Devices
AS/NZS 1715 Selection, Use and Maintenance of Respiratory
Protective Devices