## Slide 1
MANAGING NOISE AND PREVENTING HEARING LOSS AT WORK
WORK HEALTH AND SAFETY OFFICER

## Slide 2: Assessment Criteria
Describe basic mechanisms of sound and the anatomy of hearing.
Identify hazardous noise and describe its’ effects on health and safety.
Identify and describe the work, health and safety legislation applicable to management of noise hazards at work.
Describe how noise hazards are assessed, evaluated and controlled

## Slide 3: Noise
Noise at the workplace that exceeds the exposure standard and is not controlled is a major cause of hearing loss to workers.
A person conducting a business or undertaking (PCBU) must ensure that workers are not exposed to noise that exceeds the exposure standard for noise. The exposure standard for noise is defined in the WHS Regulation 2011 as LAeq,8h of 85 dB(A) or an LC,peak of 140 dB(C).

## Slide 4: Legislation
WHS Regulation 2011
Part 3.1 Managing risk to health and safety, sections 32 to 38
Part 3.2 General workplace management
Division 5 Personal protective equipment (PPE), sections 44 to 47
Part 4.1 Noise, sections 56 to 59

## Slide 5: Sound
The unique characteristics of sound are provided by a combination of three features:
Frequency
Relative intensity
Rate of onset and decay
The two properties of sound that are most often measured are frequency and relative intensity. These are explained in more details as follows:
Frequency & hertz
Relative intensity & decibel

## Slide 6: Frequency and Hertz
Frequency expresses the number of waves per second in units of hertz (Hz).
Relative intensity & Decibel
Relative intensity is presented as a sound level using a logarithmic unit called a decibel (dB).

## Slide 7: Decibel Weighting Scales
The ear does not have an equal response across the whole frequency spectrum. It best responds in the middle frequencies. For this reason adjustments, called weightings, are made to reflect the range of the human ear:
    A-weighting
    C-weighting

## Slide 8
Noise
Noise is generally described as unwanted sound. This is a somewhat subjective concept, whether a sound is unwanted is dependent on the listener. For example, personal taste in music.
Hazardous Noise
Hazardous noise means noise that exceeds the exposure standards for noise in the workplace and has the potential to cause harm to workers and others.

## Slide 9: Anatomy of hearing
The human ear is a delicate organ that can detect a wide range of sounds. However, excessive noise can permanently damage its ability to work properly.
The ear is divided into three parts:
Outer Ear
Middle Ear
Inner Ear

## Slide 10: Effects of noise on hearing
Noise can:
cause hearing loss
annoy and interfere with speech
interfere with concentration and thought processes
disturb sleep
cause fatigue and aggression
reduce immune response
lead to heart disease.

## Slide 11: Types of hearing loss
Long-term hearing loss
Immediate hearing loss
Tinnitus
Noise induced hearing loss
Indicators that a person’s hearing may be at risk:
needed to use a raised voice in a noisy workplace when talking to someone about one metre away
experiencing a dulling of hearing at the end of a working shift
ringing in the ears (tinnitus) during or after work.

## Slide 12: Audiometric Testing
The hearing of workers exposed to noise can be assessed and monitored through regular audiometric tests. Testing is an important part of a hearing conservation program to manage risks from noise exposure in a workplace. Any changes in a person's hearing levels revealed by audiometric testing should be investigated as to their cause(s) and the need for corrective action.

## Slide 13: Risk assessment
A noise risk assessment should be carried out when workers and others may be exposed to excessive noise levels. To assess noise levels a sound level meter or noise dose meter should be used. These meters are designed to measure a frequency-weighted and time-weighted value of the sound pressure level.

## Slide 14: Daily noise exposure
80 dB(A) for 8 hours will result in significant hearing loss to 5% of the work force;
85 dB(A) for 8 hours will result in significant hearing loss for approximately 10% of the work force;
90 dB(A) for 8 hours will result in significant hearing loss to 25% of the work force.

## Slide 15: Noise control policy
An important step in managing noise in the workplace is the development of a noise control policy, which should cover:
goals for noise exposure and peak noise levels
design goals for new workplaces and plant
selection and purchase of quiet plant
noise controls for temporary work areas and situations
agreements with contractors for the responsibility of noise control and provision of information
audiometric testing and availability of records
implementing a hearing conservation program

## Slide 16: Risk control
Noise control measures are required to be implemented according to the hierarchy of control so far as reasonably practicable. Elimination and Engineering are preferred because they reduce a person’s exposure to noise and do not rely on the person to wear hearing protection. Although personal hearing protection will reduce the risk from exposure to excessive noise, they do not actually reduce the noise levels.