## Slide 1: SILICONES
CC P&D – PROCESSES AND PROCEDURES

## Slide 2: Silicones
Silicones are inert, synthetic compounds with a variety of forms and uses. Typically heat resistant and rubber like, they are used in sealants, adhesives, lubricants, medical applications (e.g. breast implants), cookware and insulation.
Silicones are polymers that include silicon together with carbon, hydrogen, oxygen and sometimes other chemicals elements. Some common forms include silicone oil, silicone grease, silicone rubber, and silicone resin.
Some of the useful properties of silicones include:
  low thermal conductivity.
  low chemical reactivity.
  low toxicity.
  thermal stability.
  ability to repel water and form watertight seals.
  good adherence.
  does not support microbiological growth.
  excellent resistance to oxygen, ozone and ultraviolet light.

## Slide 3: Documents
  Hazardous Substances Register
  Safety Data Sheet (SDS) (Qld)
  PPE- Long sleeves
  Safety glasses and gloves in some cases
  Respirators in some cases
  Managing the Risk of Hazardous Chemicals in the Workplace Code of Practice 2013 (QLD)

## Slide 4: SDS & Risk Assessment
An SDS must be obtained from the supplier for the product and it must be readily accessible to the workers who will be using, handling, storing or be exposed to the chemical in the workplace.
A risk assessment has to be conducted to identify potential hazards or risks from hazardous chemicals.
Work health and safety legislation states that this must be done before the product can be used in the workplace.
Both of these documents are available on the CC Intranet for any hazardous chemicals approved for use.
If you do not have access to these documents or the chemical is not listed on the intranet site you must not use it and speak to your supervisor for further direction.

## Slide 5: Using Silicone Products
Toxicological Information
  No adverse health effects are expected if the product is handled in accordance with the directions on the product label.
Symptoms or effects that may arise if the product is mishandled and overexposure occurs are:
  Inhalation – Vapours are harmful if inhaled. A respiratory sensitiser. Can cause possible allergic reactions.
  Skin Contact – Contact with skin may result in irritation
  Eye Contact – May be an eye irritant
  Ingestion- Swallowing can result in nausea, vomiting and irritation of the gastrointestinal tract.

## Slide 6: Exposure Control & PPE
Exposure controls and PPE recommended by manufacturers within the SDS have been created for workers who are routinely, potentially exposed to the product during manufacture. If directions for use on the product label are followed then exposure for individuals should never exceed the Exposure Standards.

## Slide 7: Handling & Storage
Handling
  Avoid skin and eye contact and inhalation of vapour
Storage
  Store in a cool, dry, well ventilated place out of direct sunlight.
  Store away from alcohols, acids and bases.
  Keep containers tightly closed when not in use – check regularly for leaks.

## Slide 8: Fire Fighting
When burning, silicone may emit toxic fumes.
Fire can be extinguished with dry chemical extinguisher, fine water spray or foam.

## Slide 9: First Aid
If poisoning occurs, contact a doctor or Poisons Information Centre 131 126.
Eyes
  Flush eyes with plenty of water for at least 15 minutes. In all cases of eye contamination it is a sensible precaution to seek medical advice.
Inhalation
  Remove victim from exposure, seek medical advice if person is having trouble breathing. In the quantities CC workers use, silicone has no inhalation risks when used according to directions.
Skin contact
  If skin or hair contact occurs, remove contaminated clothing and flush skin and hair with running water. If irritation occurs seek medical advice.
Ingestion
  Rinse mouth with water. If swallowed do not induce vomiting. Give a glass of water to drink.

## Slide 10: Spills
Wipe up with absorbent cloth or rag absorb with sand or soil and dispose of in the appropriate bin.

## Slide 11: Health Monitoring
Health monitoring is not required.