## Slide 1: Determine Compliance Solutions within the NCC
CPCCBC5001 - Apply building codes and standards to the construction process for Type B construction

## Slide 2: 2.1 Determine Performance Solutions to meet the Performance Requirements
Determine Compliance Solutions within the NCC
A Performance Solution is one of the choices to achieve compliance with the Performance Requirements of the NCC.
A Deemed-to-Satisfy (DTS) Solution (also known as a Prescriptive Solution) is a standard way to demonstrate compliance with the Performance Requirements. However, there are times when a DTS Solution to a given problem does not exist or does not apply to certain building designs. Sometimes, a unique or site-specific solution is preferred or necessary. In these instances, a Performance Solution may be developed and used.

## Slide 3: 2.1 Determine Performance Solutions to meet the Performance Requirements
Determine Compliance Solutions within the NCC
A Performance Solution provides a tailored solution to meet the objectives of the Performance Requirements. A Performance Solution is said to have achieved compliance with the NCC if it has:
complied with all relevant Performance Requirements; or
demonstrated that it is at least equivalent to DTS provisions.
The use of Performance Solution as a compliance method permits the following:
flexibility in the design regarding the use of alternative materials and forms of construction or design to meet the DTS Provisions;
innovation in the use of materials, forms of construction or design; and
development of own solutions in response to unique design challenges.

## Slide 4: 2.1 Determine Performance Solutions to meet the Performance Requirements
Determine Compliance Solutions within the NCC
It must also have been assessed according to the relevant Assessment Methods discussed in Section 1.4.1. These are the following:
Evidence of suitability
Expert judgement
Verification methods
Comparison with Deemed-to-Satisfy Provisions

## Slide 5: 2.1 Determine Performance Solutions to meet the Performance Requirements
Determine Compliance Solutions within the NCC
Choosing a Performance Solution as your compliance solution has several advantages, including the following:
A Performance Solution may achieve better outcomes in terms of cost and performance because it is possible to exceed minimum requirements.
New construction techniques and emerging technology are factored in. This makes it possible to respond more quickly to the changes in the building and construction industry.
The flexibility provided by Performance Solutions means that you can develop your options. This allows you to cater to a wide range of problems, including those that are not covered by the DTS Provisions.
A Performance Solution may overcome limitations in your site.

## Slide 6: 2.1 Determine Performance Solutions to meet the Performance Requirements
Determine Compliance Solutions within the NCC
To understand Performance Solutions better, a simple example is provided below:
A Performance Requirement on access and egress of a building requires you to provide designated carparking spaces that are easy to find for people with a disability. This requirement ensures that consideration for the movement and needs of people with a disability are integrated into the design of the building.
Notice that the Performance Requirement does not state specific dimensions or materials to be used in constructing the carparking spaces. It only states that the designated spaces must be easy to find for people with a disability. It presents an outcome rather than a quantifiable requirement.

## Slide 7: 2.1 Determine Performance Solutions to meet the Performance Requirements
Determine Compliance Solutions within the NCC
Considering this, you can propose a Performance Solution that works within these parameters. You may propose to construct carparking spaces that are:
marked clearly with signs using white paint; and
placed within 5 meters of the exits and entrances of a building.
This is how Performance Solutions work.

## Slide 8: 2.2.1 Key Stakeholders
Determine Compliance Solutions within the NCC
Stakeholders are individuals who:
are actively involved with the work of the project; or
have something to gain or lose (either directly or indirectly and/or short-term or long-term) as a result of the project.
Not all stakeholders have the ability to affect the decisions of the project directly. As such, it is crucial that you correctly identify the key stakeholders who can influence the project and to what extent. These are the people you have to work and discuss options with primarily. Key stakeholders can be classified as either internal or external.

## Slide 9: 2.2.1 Key Stakeholders
Determine Compliance Solutions within the NCC
On the other hand, external stakeholders include:
the Appropriate Authority
government authorities
outsourced project team members such as contractors, subcontractors and subject matter experts (SMEs)
suppliers
In the next part, you will learn about the roles of each stakeholder and the opportunities that they present in a building project.

## Slide 10: Top management
Determine Compliance Solutions within the NCC
Choices on budget, specifications, suppliers and approach to solutions heavily depend on the overall priorities and strategies of the organisation set by the top management.
Top management refers to the president, vice-president, directors, divisions, executive board members and other such individuals. They direct the strategy and development of an organisation. They are responsible for approving in-depth plans and major milestones during the project's planning and design phases.
It may not be necessary to report every minor detail of the compliance option development to them. You will have to coordinate with them regarding the information that they need and how often you need to report. At the least, they must be kept informed of project risks, potential impacts and major decisions at all times.
Effective communication with top management is key to obtaining their support. This will expand your options and make it easier to hire better staff and obtain more resources for your project.

## Slide 11: The project team
Determine Compliance Solutions within the NCC
The project team is composed of individuals dedicated to working on the project, including those that are ‘borrowed’ on a part-time basis (for example, individuals working on another project at the time). The team includes, but are not limited to, the following:
architects
engineers
design specialists
building design professionals
trade practitioners

## Slide 12: The project team
Determine Compliance Solutions within the NCC
The team mostly has the technical knowledge and expertise. As such, their input will be required on cost, buildability, health and safety and such other technical aspects of the project. They will be able to help assess options and determine which ones may have to be eliminated to make way for the optimal one.

## Slide 13: Project manager
Determine Compliance Solutions within the NCC
The project manager is responsible for leading the project team and ensuring that they are equipped with the necessary resources to complete the project. They are responsible for guiding the discussions within the project team and handling any disputes and disagreements that may arise.

## Slide 14: Clients
Determine Compliance Solutions within the NCC
The clients are the individuals, companies or government entities who commissioned the building project. They hold power to accept or reject your chosen solution. They also affect crucial decisions of the project, such as specifications, deadlines and budgets. As such, you must always address their concerns and issues and keep them informed of any development. When considering options for the project, their preferences and needs must always be taken into consideration.

## Slide 15: Appropriate Authority
Determine Compliance Solutions within the NCC
You need to familiarise yourself with all the relevant requirements. You may engage the Appropriate Authority for expert advice on compliance issues and in identifying if a project can meet the NCC Performance Requirements.
If they deem that your proposed option (or parts of it) is non-compliant, you will have to either make the necessary changes or entirely consider other options. This can potentially have significant impacts on your deadlines and budget.
However, note that the Appropriate Authority can only provide advice. They cannot personally be engaged in developing compliance options to avoid possible conflicts of interest.

## Slide 16: Government authorities
Determine Compliance Solutions within the NCC
Government authorities are responsible for regulating the building and construction industry. They promote and enforce relevant building codes and standards and investigate alleged non-compliance. Generally, they are the ones who handle the permits and licences that you have to obtain before you can begin construction.
The government authorities you are expected to coordinate with include the following:
state and territory planning and design authorities
federal government agencies related to planning, environment and safety such as the Australian Building Codes Board and the Department of Industry, Innovation and Science
appropriate Approval Authority including building surveyors
Aside from the ones mentioned, there may also be other government authorities that you have to consider depending on which state/territory your project falls under.

## Slide 17: Outsourced project team members
Determine Compliance Solutions within the NCC
In some cases, expertise and resources are unavailable internally. Hence, work is given to individuals outside of the construction firm. This includes, but are not limited to, the following:
construction management foremen
network consultants
electricians
carpenters
architects
subject matter experts (SMEs)

## Slide 18: Outsourced project team members
Determine Compliance Solutions within the NCC
contractors
subcontractors
anyone who is not an employee of the construction firm
Outsourced members can supplement the needs and skills of the project team. They can expand your options as new perspectives and knowledge are exchanged.

## Slide 19: Suppliers
Determine Compliance Solutions within the NCC
Construction projects also depend on suppliers for construction materials such as lumber, nails, bricks and mortar. In the planning phase of developing compliance options, the role of suppliers is mostly limited to providing price quotations. These quotations can significantly affect your options, but it is not the only thing that you have to think about. There is also a wide range of factors that you must consider, including quality, reliability, service and suitability to the client’s needs. You must avoid dealing with suppliers that provide non-conforming and non-compliant building products because this can lead to safety issues within your project. Choosing the right suppliers must be done strategically to ensure the success of the project.

## Slide 20: 2.2.2 Means of Communication
Determine Compliance Solutions within the NCC
Identifying and understanding the different means of communication available to you is vital in developing strategies to engage with stakeholders. The means of communication that you choose must be suitable for the information that you wish to convey.

## Slide 21: 2.2.2 Means of Communication
Determine Compliance Solutions within the NCC
The means of communication commonly used are summarised on the following table.
Means of communication | Description
Emails | Electronic means of communication that tend to be more formal Optimal for sending files and detailed information
Face-to-face verbal communication | Includes delivery of instructions from one person to another, discussions during meetings and face-to-face negotiations

## Slide 22: 2.2.2 Means of Communication
Determine Compliance Solutions within the NCC
Means of communication | Description
Video Conference | Includes discussions made over video-calling software and smartphone applications Typically used when it is not possible to have face-to-face verbal communication due to distance and other logistical reasons
Two-way radio | Also called walkie-talkies Effective for monitoring large project sites or multi-level building projects

## Slide 23: 2.2.2 Means of Communication
Determine Compliance Solutions within the NCC
Means of communication | Description
Telephone contacts | Refer to discussions made over the telephone Similar to video conference, this is typically used when you need to communicate with people in another location

## Slide 24: 2.2.3 Strategies to Stakeholder Engagement
Determine Compliance Solutions within the NCC
Once you have determined the means of communication available, you must use these to help develop strategies to engage with your stakeholders. This will help avoid or at least minimise possible issues in your project.
The strategies below are only general guides. You must still be able to adapt and adjust accordingly to different stakeholders and situations.

## Slide 25: Identify communication barriers
Determine Compliance Solutions within the NCC
Communication barriers refer to the factors that hinder effective communication. These are some of the common barriers that you may encounter when dealing with stakeholders in a building project:
Use of construction jargons
Not all of the stakeholders that you will deal with will have a background or working knowledge of the construction industry. This makes it difficult for them to understand technical terms and specifications.
Language difference
In the construction industry, you are expected to work with a diverse group of people from different places. You will need to make use of a common language to make communication possible. However, there may be difficulties in understanding accents and overcoming the language barrier. Not everyone will have the same level of proficiency in the common language being used.

## Slide 26: Identify communication barriers
Determine Compliance Solutions within the NCC
Excessive information
There are a lot of aspects to a project and, consequently, a lot of information. The amount of information that you need to process can be overwhelming.
Inattentiveness
Being in the construction industry, you are bound to be surrounded by a lot of distractions like noise from machinery and equipment. It can be easy to get distracted by all of these and fail to communicate properly.
Using inappropriate means of communication
Sometimes, the means of communication that you used may not have been appropriate to the information that you wanted to convey. For example, you may have called for a face-to-face meeting to report something to a client when it could have been more appropriate to deliver it over a short phone call or email.

## Slide 27: Identify communication barriers
Determine Compliance Solutions within the NCC
Being aware of the common communication barriers in the building and construction industry is the first step to keeping them at a minimum. There are different methods to overcoming communication barriers. Some of these are learning how to actively listen, using simple language to make the message easier to understand and giving feedback to ensure that the message is being received correctly.

## Slide 28: Analyse stakeholders
Determine Compliance Solutions within the NCC
Stakeholder analysis refers to identifying and grouping stakeholders according to their participation, interest, and influence in the project. Methods of stakeholder analysis differ according to the needs of your project but in general, the following questions must be answered:
Who are the stakeholders?
What are their stakes in the project?
What opportunities, challenges and threats do they present?
The answers to the questions above will guide you in developing methods suitable to their problems and needs. They will help you determine how to best communicate with each of the stakeholder groups.

## Slide 29: Analyse stakeholders
Determine Compliance Solutions within the NCC
The role and level of participation of stakeholders must be defined. Note that the level of participation at different phases of the project varies. For example, a client plays a significant role in the planning and design phase of the project but has little to no role in constructing the building itself. On the other hand, a carpenter may not be able to choose the compliance option to be used for the building project. Still, they are essential to the construction part. Understanding roles and levels of participation is essential to assigning functions and ensuring there are no overlaps that can lead to inefficiencies.

## Slide 30: Understand their expectations
Determine Compliance Solutions within the NCC
Expectations must be set at the beginning of the project because it will serve as the foundation of all other decisions that will be made. It will also help you in avoiding misunderstandings and issues that may arise from it in the future.
In establishing expectations, you must remember that not all of the stakeholders you deal with will have a background on building and construction. For example, a client who wants to use a certain material for the project may not easily recognise that the material is non-complaint with the NCC. In such cases, it is your responsibility to bridge the gaps in understanding. This can be done by using simpler terminologies and doing away with explanations that are too technical to be understood by other stakeholders.
In addition, every stakeholder has different needs, demands and level of participation. Each one is going to have a different set of expectations. It is necessary to understand all of their expectations to come up with a compromise, if necessary.

## Slide 31: Keep stakeholders informed and involved
Determine Compliance Solutions within the NCC
Stakeholders must be regularly informed about the developments and problems faced, as well as the decisions made. In addition, all questions and concerns must be answered as promptly as possible.
The frequency of sending updates depends on the extent of their involvement in the project. For example, it may not be necessary to send daily updates to top management. The arrangement would have to be negotiated with the concerned stakeholder.
Aside from reporting to stakeholders, you must also solicit their perspectives and ask for their input. This can lead you to discover new perspectives or issues that can help in developing solutions. For example, a subject matter expert notices that a particular proposed solution can be improved by adding a fire-resisting element and changing some aspects of the design.

## Slide 32: IMPORTANT TO NOTE:
Determine Compliance Solutions within the NCC
There are no precise steps to be followed as to how communication with stakeholders will go, how many meetings will be conducted and how long the collaboration and negotiation process will be. These all depend on the success of initial negotiations and the degree of complexity of the proposed compliance option. It is essential that decisions made during the discussions are documented not only to monitor the progress but also to provide a historical record of the building project activities which can be reviewed when necessary.
Documentation is crucial to a project for the following reasons:
legal and contractual requirements
prevention and resolution of disputes
construction work management
for use for future projects

## Slide 33: 2.2.4 Factors to Consider in Choosing Compliance Solutions
Determine Compliance Solutions within the NCC
Performance Solutions and DTS Solutions each have their own advantages and disadvantages depending on the situation they would be applied to. In order to decide which compliance option to apply to your project, there are a number of factors that you have to consider. The next part will discuss some of the factors that can help in guiding you.

## Slide 34: Cost of development
Determine Compliance Solutions within the NCC
Performance Solutions need more resources to develop compared to DTS Solutions. This is because Performance Solutions, especially the novel ones, usually require further testing and research. This translates to additional costs, which can make the development of Performance Solutions expensive.
In deciding whether the development of Performance Solutions is worth investing in, consider both the long-term and short-term outcomes. Calculate if the savings that you would get from the efficiency of Performance Solutions can offset the costs of the development. If this is the case, Performance Solutions may be worth considering for your project.

## Slide 35: Risks and consequences
Determine Compliance Solutions within the NCC
In assessing the risks and consequences of your options, consider the following:
characteristics of the occupants that would be affected - due consideration must be given to younger occupants, older occupants and people with a disability
Fire Safety Engineering principles
principles of accessible building design
structural design principles of a building
If the risks or consequences of failure for Performance Solutions are greater, then you may need to reconsider using a DTS Solution or adjust accordingly.

## Slide 36: Client requests
Determine Compliance Solutions within the NCC
There are cases where using DTS Solutions cannot meet the expectations of the client, which makes the use of Performance Solutions the better option.
Consider the case of the renovation of a heritage building in NSW to keep up to date with the building requirements. The client requested that the building should retain its heritage features.
DTS Provision states that disability access in a lift must be wide enough for a wheelchair user to turn around inside the lift. However, applying the DTS Solution to the building means that the rooms adjacent to the lift shaft would have to be compromised and therefore, the heritage features of the building would be affected.
Given this, a Performance Solution was designed. A lift with doors on opposite sides was constructed to satisfy the NCC requirements on disability access and meet the client’s request at the same time.

## Slide 37: Existing spatial limitations
Determine Compliance Solutions within the NCC
Sometimes, you are constrained by the spatial limitations of your building. Consider the DTS Provision regarding the height of a habitable room (excluding the kitchen) which states that the height must not be less than 2.4 meters. You may not be able to comply with these for several reasons. You may be working on a heritage building with rooms lower than the height required and trying to renovate may affect the integrity of the building. Another reason is that the ceiling may have an irregular shape.
A Performance Solution may be more suitable than a DTS Solution in cases where it is difficult to overcome the existing spatial limitations within your building.

## Slide 38: Other considerations
Determine Compliance Solutions within the NCC
Aside from the factors mentioned above, there are other considerations that you need to take note of when choosing the compliance option for your project. This includes:
relevant Commonwealth, State and Territory building legislation and Australian Standards
Commonwealth anti-discrimination legislation
construction methods and buildability factors
heritage and environmental controls
occupational health and safety (OHS) policies and procedures

## Slide 39: 2.3 Apply Deemed-to-Satisfy (DTS) Solution with Supporting Evidence
Determine Compliance Solutions within the NCC
Unlike Performance Solutions that allow flexibility in developing options, DTS Solutions are prescriptive and allow little to no variation for change. A DTS Solution is achieved if you follow all appropriate DTS Provisions.
DTS Provisions are the actual clauses in the NCC. Think of DTS Provisions as steps in a ‘recipe book’ that tell you exactly what to do. They specify acceptable construction practices that have to be completed to demonstrate compliance with the NCC. They cover which materials, components, design factors and construction methods to use. DTS Solutions are foolproof and generic. They have already been deemed by regulators as acceptable practices.

## Slide 40: 2.3 Apply Deemed-to-Satisfy (DTS) Solution with Supporting Evidence
Determine Compliance Solutions within the NCC
For example, let us look at a DTS Provision D2.17 of the NCC relating to handrails. According to D2.17, a Class 9b used as a primary school must have:
one handrail fixed at a height between 865 mm; and
a second handrail fixed at a height between 665 mm and 750 mm.
Construct handrails exactly as described in the specifications above and it will comply with the NCC. This is how a DTS solution works.
To confirm that a DTS Solution complies with the relevant Performance Requirements, you may use one or a combination of the following:
Evidence of suitability is also known as a documentary evidence. It is used to support that a material, product, form of construction of design satisfies a Performance Requirement. The different examples of documentary evidence are enumerated in Section 1.4.1.
Expert judgement refers to the judgement of a suitably qualified individual or organisation.

## Slide 41: Referenced documents
Determine Compliance Solutions within the NCC
The NCC itself cannot contain all the details of every requirement for a building. This is why the NCC calls upon ‘referenced documents.’ Referenced documents have three main types:
Primary referenced documents are referenced in the NCC and are listed in Schedule 4 of the NCC. The NCC also states the edition or amendment that you have to comply with.
Secondary referenced documents are referenced in a primary referenced document. You must comply with the version or edition that existed at the time of the publication of the primary referenced document.
Other referenced documents are referenced by secondary and subsequently referenced documents.

## Slide 42: Referenced documents
Determine Compliance Solutions within the NCC
Examples of referenced documents include:
Australian Standards
ABCB protocols and standards
other publications
DTS Provisions often reference Australian Standards (AS). AS are published documents containing rules, guidelines and technical specifications. They ensure that products, services and systems are safe, reliable and able to consistently perform the way they were intended to. Before referencing an AS, you must consider:
whether the AS has been referenced in full or in part; and
the new editions and amendments in the AS.

## Slide 43: Referenced documents
Determine Compliance Solutions within the NCC
Some AS are referenced in their entirety while some are referenced only in part. If the AS is only referenced in part, then the other parts that are not referenced are considered irrelevant and have no authority. In addition, new amendments and editions of the AS are not automatically adopted by the NCC. This means that you only need to comply with the edition of the AS that was referenced.

## Slide 44: Referenced documents
Determine Compliance Solutions within the NCC
If there are any differences, including differences in definitions, between the NCC and any of the referenced documents, the NCC will overrule these differences. For more information on the NCC referenced documents, you may refer to:
NCC Part A4 for all the rules and exemptions about referenced documents; and
NCC Schedule 4 which contains a list of primary referenced documents.

## Slide 45: 2.4 Consider Performance Solutions and Supporting Evidence
Determine Compliance Solutions within the NCC
As previously mentioned, a Performance Solution is achieved by:
complying with all Performance Requirements relevant to the building project; or
demonstrating that it is at least equal with appropriate DTS Provisions.

## Slide 46: 2.4 Consider Performance Solutions and Supporting Evidence
Determine Compliance Solutions within the NCC
The compliance of Performance Solutions must be verified using one or a combination of the following Assessment Methods previously discussed in Section 1.4:
An evidence of suitability is also known as a documentary evidence. It is used to support that a material, product, form of construction or design satisfies a Performance Requirement or is equivalent to a DTS Provision.
Expert judgement refers to the judgement of a suitably qualified individual or organisation.
A verification method can be a test, inspection, calculation or any other approved verification method. It requires that the Performance Solution must achieve the set quantifiable benchmark or predetermined acceptance criteria.
A comparison with DTS provisions involves subjecting a Performance Solution and the DTS Provision to the same level of analysis and methodology.

## Slide 47: 2.4 Consider Performance Solutions and Supporting Evidence
Determine Compliance Solutions within the NCC
Assessing Performance Solutions should consider both:
the Performance Requirements that are directed addressed by the solution; and
other Performance Requirements that will be affected when they are used.
The Assessment Methods must be completed as agreed in the Performance-based Design Brief (PBDB) document, which contains details of the process of development of Performance Solutions. The results of the test(s) should also meet all the agreed acceptance criteria.
Aside from documentation of the Assessment Methods, there are also other supporting evidence that must be presented when using Performance Solutions. For example, some buildings whose fire safety requirements will be fulfilled using Performance Solutions also need to present evidence that consultations with relevant fire agencies and responding fire services have been conducted.

## Slide 48: 2.5 Document Performance-Based Solutions in accordance with Organisational Quality Procedures and Processes
Determine Compliance Solutions within the NCC
The development of Performance Solutions that can achieve compliance with the NCC Performance Requirements is a complex process. There are a lot of factors to think about such as cost, performance and suitability. Given these factors, plus the fact that Performance Solutions are commonly novel or unique to a specific situation, it is difficult to develop specific steps to follow in formulating Performance Solutions.

## Slide 49: 2.5 Document Performance-Based Solutions in accordance with Organisational Quality Procedures and Processes
Determine Compliance Solutions within the NCC
As such, the ABCB developed some guidelines that are generic and non-mandatory. These allow organisations to implement the guidelines in accordance with their own established procedures and processes to ensure that the objectives and needs of the organisation are being met.
Section 2.5 will cover what a quality management system (QMS) is and how it is established and implemented by an organisation. It will talk about the importance of good QMS documentation that is fit for the purpose for which they are created. Lastly, the process of formulating Performance Solutions, as outlined by the ABCB, will be discussed.

## Slide 50: 2.5.1 Quality Management Quality management is a
Determine Compliance Solutions within the NCC
Quality management is a crucial aspect of any building work. It involves formally establishing organisational policies, procedures and processes to ensure that the quality of your project meets or even exceeds expectations. It aims to coordinate and direct the activities of an organisation to achieve client and regulatory requirements consistently, improve effectiveness and efficiency and achieve organisational objectives and needs.
Quality management has two elements, which are as follows:
Quality assurance (QA) refers to the ‘part of quality management focused on providing confidence that quality requirements will be fulfilled.’ The assurance must be given both internally to management and externally to clients, government authorities and other third parties. QA focuses on activities related to how a process is performed or how a product is made.
Quality control (QC) refers to the actual fulfilment of the quality requirements. It focuses on the inspection element of quality management.

## Slide 51: 2.5.1 Quality Management Quality management is a
Determine Compliance Solutions within the NCC
An organisation develops its quality management system using the plan-do-check-act (PDCA) cycle. The PDCA cycle aims to identify processes that form your quality management system and determine the interaction between them. It combines planning, implementing, controlling and continual improvement into one cycle. The steps of the PDCA cycle are as follows:
Plan: Planning involves looking for the answers to the following questions:
What should be done?
How much should be done?
When is it required to be done?
Who should do it?
Where is it required to be done?

## Slide 52: 2.5.1 Quality Management Quality management is a
Determine Compliance Solutions within the NCC
Do: This involves implementing the plan.
Check: This involves monitoring the processes and measuring the outcomes according to the organisation's plans, policies and objectives.
Act: This involves taking measures and activities to improve the performance of the organisation.

## Slide 53: 2.5.1 Quality Management Quality management is a
Determine Compliance Solutions within the NCC
Effective implementation of the organisation’s quality management system has numerous benefits to a building project, including:
clarifying standards and requirements;
minimising misunderstandings and potential conflict;
satisfying the requirements of the clients and instilling confidence in the organisation;
meeting the organisation’s requirements, including compliance with relevant regulations and provision of products and services at the most cost-effective and resource-efficient manner;
lowering costs by reducing waste;
minimising the potential for error; and
defining, controlling and improving processes.

## Slide 54: 2.5.2 Development of Performance Solutions
Determine Compliance Solutions within the NCC
All organisations should develop their QMS according to its needs and goals, but the one thing they have in common is that each must maintain documentation of their QMS. Proper documentation serves as the foundation of QMS. It ensures that processes are correctly understood and consistently executed in order to deliver quality products or services to your clients. Some of the functions that a QMS documentation serves include the following:
communicating information to relevant people
providing evidence of conformity
allowing easy monitoring of processes
sharing knowledge that can be referred to by others in the future

## Slide 55: 2.5.2 Development of Performance Solutions
Determine Compliance Solutions within the NCC
In order to guide parties who are interested in formulating simple or complex Performance Solutions, the ABCB has produced some guidelines to be followed. These guidelines are not mandatory or regulatory in nature. These are only meant to provide general information as to how the process typically goes. In following the ABCB guidelines, the organisational quality management system must be considered to achieve quality policies and objectives.

## Slide 56: Coaching
Determine Compliance Solutions within the NCC
The ABCB guidelines are as follows:
Prepare a Performance-Based Design Brief
Carry out analysis, modelling or testing
Collate and evaluate results
Prepare a final report

## Slide 57: Step 1: Prepare a Performance-based Design Brief (PBDB)
Determine Compliance Solutions within the NCC
A Performance-Based Design Brief (PBDB) is a document that serves as a record of all the fundamental activities and outcomes of the Performance Solution design process as agreed during the stakeholder negotiation process. When completed, the PBDB becomes the roadmap for the proposed solution.
The PBDP must adequately demonstrate that after designing the solutions and conducting assessment methods, the relevant NCC Performance Requirements have been achieved.

## Slide 58: Step 1: Prepare a Performance-based Design Brief (PBDB)
Determine Compliance Solutions within the NCC
The contents of the final report of the PBDB typically include the following:
a summary of the proposal, including:
building type and function
height
location of the building
an explanation and description of the proposed solution
outline of the Performance Requirements that apply
the agreed analytical assessment process

## Slide 59: Step 1: Prepare a Performance-based Design Brief (PBDB)
Determine Compliance Solutions within the NCC
the agreed acceptance criteria
required scope of supporting evidence
format and content of the final report
acknowledgement of participants

## Slide 60: Step 2: Carry out analysis, modelling or testing
Determine Compliance Solutions within the NCC
In order to ensure compliance with the NCC, the proposed Performance Solution must be assessed using the appropriate Assessment Methods specified in the NCC.
The method of analysis, modelling or testing must be chosen according to what is appropriate to the complexity of your project and carried out following what is agreed by stakeholders in the PBDB.

## Slide 61: Step 2: Carry out analysis, modelling or testing
Determine Compliance Solutions within the NCC
Some of the tools that you can use to evaluate the proposed Performance Solution include the following:
comparative or absolute analysis
qualitative or quantitative analysis
deterministic or probabilistic analysis
empirical calculations
in-situ or testing in a recognised laboratory
computer-aided modelling

## Slide 62: Step 3: Collate and evaluate results
Determine Compliance Solutions within the NCC
The results from the previous step must be collated for analysis. Results from multiple trials or design scenarios may have to be considered.
After the results are collated, an analysis will be carried out to form the conclusions for the final report. The results must meet the acceptance criteria agreed in the PBDB. In the evaluation, any uncertainties and sensitivities must also be considered.
If the results are either inconsistent or unable to meet the acceptance criteria, further analysis, modelling or testing may have to be conducted.

## Slide 63: Step 4: Prepare a final report
Determine Compliance Solutions within the NCC
The final report is mandatory documentation that must clearly demonstrate compliance with the NCC Performance Requirements.
The final report commonly includes the following content:
an overview of the PBDB, including the following:
scope of the project
relevant stakeholders
applicable NCC Performance Requirements
approaches and methods of analysis
any assumptions made
acceptance criteria and safety factors agreed to by stakeholders

## Slide 64: Step 4: Prepare a final report
Determine Compliance Solutions within the NCC
overview and outline of the analysis, modelling and/or testing carried out, including:
method of analysis used
calculations and outcomes
sensitivities, redundancies and uncertainty studies carried out
the results obtained and relevance to the PBDB
evaluation of results including:
comparison of results with acceptance criteria
further sensitivity studies undertaken, if any
any expert judgement applied and its justification

## Slide 65: Step 4: Prepare a final report
Determine Compliance Solutions within the NCC
conclusion including
specifications of the final design that are deemed acceptable
the NCC Performance Requirements that were met
all limitations to the design and any conditions of use
The following documentation must be retained for a minimum 10-year period together with the relevant compliance certificate where applicable. The property owner must also be provided full copies of the Performance Solution, including the PBDB, plans, results and final report. The information contained in the documentation will be used for future works such as repairs, servicing, alteration and/or maintenance.

## Slide 66: 2.6 Complete and Compile Relevant Documentation and Evidence that Complies with NCC Performance Requirements
Determine Compliance Solutions within the NCC
Every part of a building must be constructed in an appropriate manner using materials, products and forms of construction that comply with the NCC Performance Requirements. Aside from the requirements set out by the NCC, additional conditions may also be required by the following:
other Commonwealth, State or Territory legislation
contracts that include specific quality, material or other such requirements
The NCC provides a system to establish and prove compliance with the Performance Requirements. This includes presenting documentary evidence. The form of evidence required to be presented differs according to circumstances, legislation and the Appropriate Authority, but in general, it must adequately show that all materials, products, plumbing projects and forms of construction or design are of the quality to fulfil their functions within the building.

## Slide 67: 2.6 Complete and Compile Relevant Documentation and Evidence that Complies with NCC Performance Requirements
Determine Compliance Solutions within the NCC
The hierarchy of rigor shows the suitability of each form of evidence in a given situation. The higher the option is on the list, the stronger it is as a form of evidence. Typically, innovative components or those with high consequences of failure require more vigorous options to prove compliance. On the other hand, those whose consequences of failure are low commonly require options that are low on the hierarchy of rigor.
The options for documentary evidence are discussed below according to their order in the suitability framework.

## Slide 68: CodeMark or CodeMark Australia
Determine Compliance Solutions within the NCC
Under the CodeMark or CodeMark Australia schemes, only certification bodies accredited by the Joint Accreditation System of Australia and New Zealand (JAS-ANZ) can issue Certificates of Conformity.
The CodeMark and CodeMark Australia schemes provide a nationally accepted process for demonstrating compliance with the NCC. Using the following schemes helps to:
streamline and fast-track building approvals;
support the use of new or innovative building products and systems; and
avoid having to repeat the assessment of products and systems that have already proven compliance with the NCC before.
This is the most rigorous option for proving NCC compliance. It is usually used for materials or products that have high consequences for failure.

## Slide 69: Certification of Accreditation
Determine Compliance Solutions within the NCC
This is issued by a state or territory accreditation authority under the relevant state or territory building legislation.
The Certificate of Accreditation contains the following:
verification that the properties and performance of a building component are able to fulfil specific requirements of the NCC
any conditions and limitations on the use of the building component
If you already have a Certificate of Accreditation and want to use it in another jurisdiction, you must get the Appropriate Authority’s approval first.

## Slide 70: Certificate issued by a Certification Body
Determine Compliance Solutions within the NCC
The JAS-ANZ accredits certification bodies or conformity assessment bodies (CABs). CABs can issue certificates under an industry-operated building product certification scheme.
The certificates should contain the following key details:
issuance date of the certification
duration of validity
signature of the issuing body
other relevant information

## Slide 71: Reports issued by an Accredited Testing Laboratory
Determine Compliance Solutions within the NCC
An Accredited Testing Laboratory can issue a report certifying that a particular component has been proven suitable by an appropriate test.
An Accredited Testing Laboratory can be any of the following:
a testing laboratory accredited by the National Association of Testing Authorities (NATA)
a laboratory accredited by an organisation with a mutual recognition agreement with NATA
an organisation recognised as being an Accredited Testing Laboratory under legislation at the time the test was undertaken
You may see whether a laboratory or facility is currently accredited by NATA using the register on their website.

## Slide 72: Certificate of report from a professional engineer, recognised expert or another appropriately qualified person, as appropriate
Determine Compliance Solutions within the NCC
In this option, a certification from professionals and experts can be accepted as long as:
it has a basis and can be subjected to scrutiny; and
it references relevant standards, specifications, software or other publications.

## Slide 73: Other forms of documentary evidence such as, but not limited to, a Product Technical Statement
Determine Compliance Solutions within the NCC
This documentation is the least rigorous option and often requires another supplemental documentary evidence. Evidence under this option should:
suitably describe the subject of the document;
specify the conditions that the statement of verification relies on;
describe any limitations to the statement of verification;
refer to construction and/or installation standards as necessary; and
include a reference to any standards, test reports, specifications or other publications used in suitability verification.
Before submitting this as evidence, it must first be approved by the Appropriate Authority as suitable for determining compliance. This is typically used when consequences of failure are low.

## Slide 74: Other forms of documentary evidence such as, but not limited to, a Product Technical Statement
Determine Compliance Solutions within the NCC
The options for documentary evidence are not mutually exclusive. This means that the chosen option may include elements of other options. It also means that more than one option may be required as evidence of compliance with the NCC.
The suitability of the option(s) selected will need to be approved by the Appropriate Authority. Additionally, it is also important to remember that the documentary evidence has to be current. Otherwise, it will not be accepted. The evidence is no longer considered current if it is:
expired;
attesting compliance with a superseded NCC requirement that does not apply to the project it is submitted for; or
withdrawn.

## Slide 75: What have we learned?
In this part of the session, we have covered:
Classify Buildings
Determine Compliance Solutions within the NCC
Apply Fire Protection Requirements

## Slide 76
End of Part 2