## Slide 1: Hazard Identification and Risk assessment procedure for Excavation & Trenching
Purpose and scope
This procedure outlines a process to identify hazards from undertaking Excavation & Trenching on site. It determines the risk rating on hazards related to excavations & Trenching. Implements risk controls and the process for reviewing the controls.
This procedure applies to everyone involved with JHG.

## Slide 2: Definitions
Hazard: is a situation or a thing that has the potential to hurt or harm a person
Risk: the likelihood and consequences of the hazard causing harm
A risk assessment is carried out when
There is uncertainty about how a hazard may result in injury or illness
The work activity involves a number of different hazards and there is a lack of understanding about how the hazards may interact with each other to produce new or greater risks, or
There are changes at the workplace that may impact on the effectiveness of control measures or may require new control measures such as the introduction of a new process or piece of equipment
A risk assessment is mandatory under the WHS Regulations for certain activities that are high risk

## Slide 3: Legislation & Standards
Work Health and Safety Act | COP Managing Noise and Preventing Hearing Loss at Work
Work Health and Safety Regulations | COP Plant
Environmental Protection Act | COP Excavation work
Environmental Protection Regulation | COP Mobile Crane
COP Hazardous Manual Tasks | 

## Slide 4
Procedure – Risk Assessment
1) Identify all of the risks associated with the hazard.
2) Assess the risk/s using the following Risk Assessment Matrix
3) Determine the appropriate control/s to mitigate the risk of the hazard causing harm as far as is reasonably practicable. Use the following Hierarchy of Control to implement the most effective controls. Document the results on the Risk Assessment Form.
4) Determine the priority or urgency with which the hazard should be controlled. Use the Risk Assessment Action Plan to list the hazards and track the implementation of the controls.
Here are some suggested action timelines. The risk level that remains after any applicable controls are applied is called residual risk. Our Goal is to Minimise the Risk to Low as possible by implementing Control measures
Risk action priority
Extreme Risk – immediate action required
Very High Risk – prioritised action within a month
High Risk – prioritised action within three months
Medium Risk – planned action required
Low Risk – manage with current procedures

## Slide 5
Risk assessment matrix
The following table provides a Risk Rating once the Likelihood and Consequence are determined:
 |  |  |  | CONSEQUENCES |  |  |  |  |  |  |  | 
 |  |  |  | Insignificant [1] |  |  | Minor [2] |  | Moderate [3] | Major [4] | Catastrophic [5] | 
LIKELIHOOD | Almost Certain [5] |  |  | Moderate (5) |  |  | High (10) |  | High (15) | Catastrophic (20) | Catastrophic (25) | 
 | Likely [4] |  |  | Moderate (4) |  |  | Moderate (8) |  | High (12) | Catastrophic (16) | Catastrophic (20) | 
 | Possible [3] |  |  | Low (3) |  |  | Moderate (6) |  | Moderate (9) | High (12) | High (15) | 
 | Unlikely [2] |  |  | Low (2) |  |  | Moderate (4) |  | Moderate (6) | Moderate (8) | High (10) | 
 | Rare [1] |  |  | Low (1) |  |  | Low (2) |  | Low (3) | Moderate (4) | Moderate (5) | 
 |  | If the residual risk | = |  | Catastrophic (16+) | then |  | Work unable to proceed seek other methods (Significant) |  |  |  | 
 |  |  | = |  | High (10 – 15) | then |  | Permission from high level management for work to proceed (Significant) |  |  |  | 
 |  |  | = |  | Moderate (4 – 9) | then |  | Permission from worker in charge for work to proceed (Insignificant) |  |  |  | 
 |  |  | = |  | Low (1 – 3) | then |  | Work able to proceed (Insignificant) |  |  |  | 

## Slide 6
Level 1
Eliminate the hazards
Level 2
Substitute the hazard with something safer
Isolate the hazard from people
Reduce the risks through engineering controls
Level 3
Reduce exposure to the hazard using administrative controls
Use personal protective equipment
MOST
LEAST
Reliability of control measures
HIGHEST
LOWEST
Level of health and safety protection
Risk control
Where a risk to health & safety has been identified, controls must be introduced to reduce risk levels to an acceptable level. When introducing a control measure, consideration should be given to what is “practicable” in each instance.
The following Hierarchy of Control, to control the risk should be adopted.
Elimination of the hazard or risk (most effective)
Substitution of the plant or activity to one with a lower level of risk
Engineering redesign or alter the plant or equipment to ensure the work is performed safely
Administrative procedures/ instructions to ensure the work is performed safely
Personal Protective Equipment (PPE) should always be the last control option (least effective)
A combination of controls may be appropriate, however the solution should follow the Hierarchy of Control.

## Slide 7: Trench Collapse Resulting From Excavation Trenching
Hazard Identified
L | C | R
3 | 5 | 15
Before Controls are Implemented
After Controls are Implemented
L | C | R
2 | 4 | 8
Controls To Implement
Obtain Permit Prior to Commencing excavation Tasks
Authorised personnel only in area – use fencing and signage
Nominated personnel to inspect and assess ground conditions regularly.
Shore, bench and batter as required. As a minimum, excavations below 1.5 m require benching of 1 vertical to 1 horizontal or battering of 1:1.
Excavated spoil to be placed so that there is no likelihood of it falling into excavated area i.e. 600mm away.
Heavy machinery to be kept away from the edge of excavated surfaces to avoid slope failure.
Person's Responsible to Ensure Implementation of Controls
Supervisor

## Slide 8: Trench Collapse WHAT NOT TO DO

## Slide 9: Examples of Correct Trenching Practices

## Slide 10: Review Of Control Measures
You must review your risk control measures:
when the control measure is not working (eg when someone is injured or experiences a ‘near miss’)
before workplace layout or practices are changed
when new equipment, materials or work processes are introduced
if a new problem is found
if consultation shows a review is necessary
if there is an injury or near miss
if a health and safety representative requests it.
Review Process to be conducted Using Site Inspection Checklist Provided
SAFETY IS EVERYONES PRIORITY