## Slide 1
PREVENTING MUSCULOSKELETAL DISORDERS
WORK HEALTH AND SAFETY OFFICER

## Slide 2: Assessment Criteria
Identify the relevant Queensland Work Health and Safety legislation specifically the hazardous manual tasks regulation and code of practice
Apply risk management strategies for hazardous manual tasks
Identify the relevant Queensland Work Health and Safety legislation relating to STFAL in the current Regulations and code of practice.
Understand how STFAL occur
Understand and identify common occupational STFAL hazards and influencing factors
Understand how to manage occupational STFAL risks

## Slide 3: What is ergonomics?
Ergonomics is the scientific study of human work and the interaction between workers, tools and the environment. The term ergonomics is derived from the Greek words “ergos” meaning work and “nomos” meaning natural law. Ergonomics is an applied science with knowledge drawn from psychology, biology, medicine and engineering.

## Slide 5: Economics of Ergonomics

## Slide 6: Musculoskeletal Disorders
Sprains and Strains

## Slide 7: Legislation
WHS Act
WHS Regulation
Hazardous Manual Tasks Code of Practice 2011(HMTCOP 2011)
Manual Tasks Involving the Handling of People Code of Practice 2001

## Slide 8: Risk Management

## Slide 9: What is required to manage the risk?

## Slide 10: Identifying HMT’s
Workers who perform manual tasks can provide valuable information about discomfort, muscular aches and pains that can signal potential hazards. For example, you could ask workers to identify tasks that:
are difficult to do (or appear harder than they should be)
are very tiring (muscle fatigue reduces work capacity)
are awkward or dangerous (for example, difficulty controlling loads)
cause discomfort.

## Slide 11: Sources of risk
The main sources of risk are:
work area design and layout
the nature, size, weight or number of things handled in performing the manual task,
systems of work
the environment in which the manual task is performed.

## Slide 12: Controlling the risks

## Slide 13: Changing the design or layout

## Slide 14: Changing the nature of the work

## Slide 15: Administrative Controls
Lifting technique training not effective
Job rotation
Team handling
Work environment

## Slide 16
PREVENTING MUSCULOSKELETAL DISORDERS
SLIPS, TRIPS AND FALLS AT LEVEL
WORK HEALTH AND SAFETY OFFICER

## Slide 17: Assessment Criteria
Identify the relevant Queensland Work Health and Safety legislation relating to STFAL in the current Regulations and code of practice.
Understand how STFAL occur
Understand and identify common occupational STFAL hazards and influencing factors
Understand how to manage occupational STFAL risks

## Slide 18: STFAL relevant legislation
WHS Act S19 Primary duty of care
WHS Act S21 Management or control of fixtures, fitting or plant at workplace
Managing the work environment and facilities COP 2011
WHS Regs 40 General workplace facilities
Notes: 18
WHS Regs Handouts
S40 Duty in relation to general workplace facilities
A person conducting a business or undertaking at a workplace must ensure, so far as is reasonably practicable, the following—
(a) the layout of the workplace allows, and the workplace is maintained so as to allow, for persons to enter and exit and to move about without risk to health and safety, both under normal working conditions and in an emergency;
(b) work areas have space for work to be carried out without risk to health and safety;
(c) floors and other surfaces are designed, installed and maintained to allow work to be carried out without risk to health and safety;
(d) lighting enables—
  (i) each worker to carry out work without risk to health and safety; and
  (ii) persons to move within the workplace without risk to health and safety; and
If not covered in above apply
-WHS Act S19 Primary duty of care
-WHS Act S21 Management or control of fixtures, fitting or plant at workplace (plus S32/32) eg for landlord, body corporate
Managing the work environment and facilities 2011 COP esp. section 2 the work environment
- access ways, housekeeping, work areas, floors and other surfaces, workstations, lighting

## Slide 19: Mechanism
Slip
Misstep
Near other hazards
Slip or trip without falling
Trip
Notes: STFAL commonly caused by slips, trips, misstepping on stairs
Slip: occur when there is not enough grip (friction) between foot/shoe and walking surface, most commonly during heel strike and you lose your balance
Trip: When your foot (or lower leg) hits an object and your upper body continues moving, throwing you off balance
Misstep: commonly when you step down unexpectedly to a lower surface and lose your balance i.e. not seeing bottom step (often involve stairs)
Near other hazards: hot (deep fryer), sharp (knives), hard (edge of table), hazardous substance, at height (stairs) or adjacent to mobile plant, can result in greater consequences.
Check out Gavin McGuane’s story: He tripped and ended up spraying cleaning fluid into his eyes and permanently blinded him
Notwithstanding this serious incident, STFAL can result in serious injury without involving an adjacent hazard. STFAL can involve sudden/high acceleration impact on the body
Loss of balance and no fall can still result in injuries (often not included in STFAL data, in US this accounted for 4.4% of non fatal occupational injuries)
Ask group: What types of injuries result from STFAL?
STFAL can cause: fractures, bruises, lacerations, dislocations, concussion, permanent injuries or death

## Slide 20: What are the risk factors?
Notes: Following incidents, we see at many workplace identify only a couple of factors that contribute to slips and falls e.g. workers not paying attention, slippery floors. This leads to workplaces to focus on these factors to when controlling the risk (such as after incidents).
Share a case study of:
  a young fast food worker who sustaining horrific burns after slipping and falling, being drenched in several litres of 160C oil drained from a deep fryer
  The work was hospitalised for several days, requiring skin grafts on her arms and legs, suffered severe pain, and became anxious and socially withdrawn after being doused in the dangerous liquid.
  Towards the end of operating hours, the oil from the deep fryer is decanted into the blue bucket positioned on the floor
  This practice had been occurring for a number of months and accepted by the supervisor/manager as standard practice.
  The tiled area you can see, is the main thoroughfare for staff to prepare food and to access other areas of the store.
  ASK: What do you think are the risk factors in this case? Each participant to nominate one risk factor. See sheet
  Floor oily from deep fryer, decanting oil into bucket, humidity from deep fryer
  Slip resistance of flooring could be low due to wear and tear, floor not being cleaned properly (regular and periodic deep clean),
  Rushing due to lots of customers, New worker not know that floor is slippery
  Only required to wear closed in footwear, not checked for good condition
  Poor visibility of spots of oil, lighting, colours of tiles
  Why was unlidded hot oil container on the floor
  Tight area to walk due to clutter and bucket
We can group the risk factors into a number of categories e.g. work area, work task, worker, organisational/systems factors (lead to STFAL risk factor model)

## Slide 21: STFAL risk factors
Notes: Like many other hazards, STFAL usually involves a combination of factors rather than a single issue that contribute to an incident
They will not all be significant in every case, but need to be considered to clearly ID/assess then more effectively control STFAL risks
This model is based on good work design which looks at the work area, work activity, workers and way work is organised.
Traditionally the focus has been on work area eg flooring, but we know that it wider than this.
For STFAL we also acknowledge the external factors that impact on the risk factors as seen in this diagram.
Let’s discuss the risk factors and areas in next slides. The information we are going over now is covered in your notes

## Slide 22: Work area
Walking/ground surface
Slip resistance
  Needs to be adequate for activity, expected contamination and expected pedestrians
  Can be lower in spots
  Change between floor surfaces
  More info in Australian Standards
Linked to quality of cleaning
Notes: For safe walking we need:
Sufficient grip between floor/ground surface and your feet
Smooth even level surfaces
Slip resistance (amount of “grip” of walking surface):
needs to be adequate for expected activity, amount and type of contamination, people walking in the area
Can be objectively measured with testing equipment e.g. Pendulum as per Australian standard method, slip alert
Is just one of the risk factors, many focus on the number rather the combination of risk factors
Part of flooring with low slip resistance (e.g. grate covers) even if other parts of flooring with sufficient grip
Can Change between different floor surfaces

## Slide 23: Work area
Includes rain/ weather
Some types more slippery than others (dusty, water based, oily, greasy, semi-solid, mud)
Recurrence after cleaning (Are cleaning procedures keeping up?)
Water and other contaminants
Notes: Research has shown that the presence of contaminants increase the risk of slips by 14.6 times
Contaminants can be considered any substance or waste on the floor/ground surface
Water and other contamination (includes rain/weather)
type – dry/dusty, water based, oily, greasy, semi-solid (e.g. moss, food), mud
  Greater viscosity greater risk of slipping e.g. grease compared with water
amount (very light/light/medium/heavy),
recurrence after cleaning (indicates cleaning procedure not keeping up)
consider source of contamination, external and internal areas

## Slide 24: Work area
Cleaning (practice/systems)
Correct method for type of flooring (manufacturers’ instructions)
Adequate for amount/type of contamination
Cleaning equipment – is clean & in good order
Scheduled with minimal pedestrian traffic
Effectively keeps pedestrians off till fully clean and dry
Spills attended to promptly
Notes: Cleaning (practice/systems) linked closely with contamination
  correct method for type of flooring (manufacturers’ instructions)
  Adequate for amount/type of contamination (no excess residue, periodic deep clean)
  Cleaning equipment – is it clean & in good order? E.g. dirty brooms/mop
  Scheduled with minimal pedestrian traffic, eg only cleaning half of the walkway at one time so have dry area for pedestrians to walk on
  Effectively keep pedestrians off till fully clean & dry eg barricades/cones with chains
  Spills attended to promptly – spills management policy/finders keepers

## Slide 25
  Holes, protrusions, rough ground, uneven paths, curled edge of lino
  Stairs and ramp dimensions consistent/within AS 1657 dimensions
  Handrails – ease of use and position
Surface/structural irregularities
Subway video
Work area
Notes: Level, even and smooth surfaces are needed for safe walking
common causes of uneven surfaces
  Loose floor surfaces (mats, tiles, edge of carpet)
  Pot holes, missing grate covers
Look at video on stair design (click on sub-way video)
Safer walking on stairs requires:
Consistent stair geometry/dimension that are consistent with AS 1657
  Subway video is a great example of less than a cm consistently tripped people up
Questions to ask when using stairs – does it feel consistent and not awkward to use?
May need to carefully measure each step
Check nosing on stairs are non-slip, not rounded, not rough (can trip)
Handrails on stairs and ramps
  Need to be easy to reach and use
  Consistent within AS 1657

## Slide 26
Items left out/incorrectly stored/cluttered e.g. pallets
Cords and other items are left on the floor
Temporary obstacles
Housekeeping
Walkways/work areas unmarked
Areas left unclean & cluttered
Flooring is in a poor state of repair
Spills and other contaminants/ waste left where they fall
Work area
Notes: Temporary obstacles include:
items left out/incorrectly stored/cluttered e.g. pallets
cords and other items are left on the floor
walkways used as storage areas, need adequate storage
Housekeeping
areas left unclean
flooring is in a poor state of repair
spills and other contaminants/waste left where they fall

## Slide 27
Visibility/detectability of hazard
Greater risk when hazard:
unexpected
cannot be easily seen
blends into surroundings
Need:
adequate and even lighting to clearly see hazard/changes
clearly marked edge of stair/step, change in floor surfaces, start/end of ramp and surface hazard
Work area
Notes: No matter how good the floor is, if you can’t see where you are going there is always the risk that someone might slip and fall
Greater risk when hazard:
unexpected
cannot be easily seen
blends into surroundings
Visibility/detectability of hazard
  Adequate and even lighting to clearly see path of travel and hazard/changes
  Can easily see edge of stair/step, change in floor surfaces, start/end of ramp
  If unable to remove, highlight hazards e.g. yellow paint
  Also check if anything else will distract from paying attention to hazards e.g. loud noises, assisting someone e.g. patient

## Slide 28: Scary stairs gallery
Notes: Where is the edge of the step?
How steep are the stairs?
Other scary stairs images welcome

## Slide 29
Load handling (carrying, pushing, pulling)
Pace of work/time pressure/scheduling
Attentional demands
Interaction of other workers/
other activities
Work activity
Notes: What are aspects of the task that impact on safe walking?

## Slide 30
Footwear
Individual characteristics and experience
Workers/others
Notes: Footwear - Important but not only control measure
suitable footwear can provide good grip on floor during work activity (and expected contaminants)
Inappropriate footwear increases risks (e.g. office staff wearing dress shoes through warehouse)
suitable shoes:
  Have non-slip soles (to provide grip when walking)
  Keep treads clean (clogged treads do not provide the grip needed)
  Make sure they fit well (for comfort and for better grip when walking)
For some work areas may need more slip-resistant footwear depending on level and type of contaminants. Trial first before buying for all workers.
  Good tread pattern and a flexible sole is important. Better with well-defined tread pattern (the more edges, ,the firmer the grip) Please refer to AS 2210 and HSE footwear guide. More info on web site
Let’s look at the sole of our own shoes…
Individual characteristics can influence their needs to safely walk
Who will be walking in the area: office staff, customers, patients, members of the public?
Mobility, strength, cognitive ability, visual ability, fatigue, medication etc.. footwear (Reports of people using multi-focals or even bi-focals complain about not able to see changes in surface/step perception
Experience
Experience/familiarity with work task & work area e.g. know area near back stairs prone to poor drainage

## Slide 31: Organisations factors/Systems of work
Work planning (current and future)
Production demands/incentives
Maintenance
Training
Supervision
Notes: the way the work is organised
Work planning (current & future)
Safe work procedures e.g. routes and equipment used
work hours/fatigue
Staffing level (e.g. peak times), skill mix, shift arrangements
Workers control/input into how work is done
Production demands/ incentives:
increase pace (finish & go, per piece payment)
Time pressures/deadlines
Maintenance
proactive or only reactive
equipment e.g. leaks
flooring/access ways
Training: Knowledge of STFAL risks and how to control e.g. why spillages cause injury and importance of keeping people off floors till fully dry
Supervision: STFAL controls used properly & Cleaning procedures followed

## Slide 32: External factors (that impact on STFAL risks)
Landlord/other tenants
Customer/customer site/sub-contractor
Designers/manufacturers/
suppliers/installers
Notes: landlord often responsible for fittings, fixtures and plant at the workplace e.g. flooring, cold room, refrigeration. Check lease agreements
other tenants can create hazards e.g. leakage onto common area
body corporate - responsible for common area e.g. lighting, cleaning
designers - specifying flooring or designing out trip hazards
manufacturers/suppliers/installers e.g. through flooring that meets slip resistance criteria, products/equipment that do not contaminant
supply chain/customers can contribute to STFAL e.g. timeframes for work to be completed can increase, STFAL hazards when working at customer site
sub-contractors activities can create STFAL hazards e.g. truck washing sub-contractor floods access areas

## Slide 33: Ways to reduce risks
Eliminate surface/structural irregularities
Design out/remove hazards
Replace surface
Provide safe stairs/ramps/handrails
Check dimensions
Check and reduce slipperiness of
walking surface
Correct flooring for use
Cleaning procedures

## Slide 34: Ways to reduce risks
Stop/contain water and other contaminants (including rain)
Drainage and maintenance
Absorb it, cover it, bin it
Keep floors dry and clean, keep people off floor till dry
Cleaning methods, products and equipment
Routine management
Barricades, signage
Keep walkways/work areas clear
Remove obstacles
Sufficient storage and bins
Notes: Extra notes on design improvements:
Design AS 1657 fixed platforms, walkways, stairways and ladders – design construction and installation
Slip resistance of floor surfaces
Drainage – appropriate drainage without excess angle creating increased slip hazard
Level floor surfaces
Elimination of isolated steps and other isolated trip hazards
Design of rise and going of stairs
Recess shower hobs
Recess or rebating sliding door frames into concrete slab
Plenty of storage areas
Adequate space around work areas/stations
Lighting plan to ensure adequate and even lighting

## Slide 35: Ways to reduce risks
Improve visibility/detectability of hazard
Highlight, eg, paint step edge yellow
Adequate and even lighting
Plan for safe work (current and future)
Load handling, scheduling, route
Mobile phone policy
Wear suitable shoes
Communicate, train and supervise

## Slide 36: STFAL resources
MSD Resource sheet – Slips, trips & falls
STFAL checklists
www.worksafe.qld.gov.au
www.hse.gov.uk/slips/