## Slide 1
WELDING
WORK HEALTH AND SAFETY OFFICER

## Slide 2: Assessment Criteria
Describe the statutory and minimum requirements relating to welding processes.
List the hazards that are associated with the processes of welding.
Describe the control measures that are available to minimise or remove the risk associated with these hazards.

## Slide 3: Welding techniques
Shielded Metal Arc
Gas Metal Arc
Gas Tungsten Arc
Oxy-fuel
Welding hazards include electric shock, burns, fire and explosions, radiation, heat, fumes & gases, noise and numerous other physical hazards.

## Slide 4: Gas welding safety
Storage and handling
General gas welding safety tips
Personal protective equipment
Proper ventilation

## Slide 5: Welding – Electrical Safety
Servicing and installation must only be undertaken by a qualified licensed electrician. Never tamper with electrical supply circuits or systems. The welder is only responsible for making connections in the welding circuit and for setting external welding machine controls.
Equipment should be well maintained and checked regularly, particularly the insulation and connections on work return leads and holders.
Wherever possible work should be performed on a dry insulated floor. Wooden platforms, rubber mats, or dry areas provide extra protection especially in confined spaces.

## Slide 6: Welding – Electrical Safety
Electrodes or welding wire should never be touched with bare hands when in the holder or welding gun. Holders or welding guns should never be held under the armpits. Remember, hot work increases risk due to the reduced skin resistance when sweating occurs.
Always use Australian Standards - approved welding helmets and lenses.
Where practicable consideration should be given to the use of Welding Voltage Reducers that maintain an output no greater than 12v until the arc is struck.

## Slide 7: Burns, fire and explosion
Flame cutting and welding operations are a major cause of industrial fires. The precautions necessary to avoid such incidents depend largely upon the processes being used and the location of the work.

## Slide 8: Fumes and gases
During the welding process certain health and safety hazards may be present in the form of metal fumes and gases.
General ventilation, local point exhaust and personal respiratory protection all serve to remove or reduce risk to the worker.

## Slide 9: Control measures
General or dilution ventilation
Local exhaust ventilaton

## Slide 10: Physical hazards
Always use proper supports.
Ensure that you are comfortable.
Always wear suitable eye protection which protect the eyes from radiation. For added protection from foreign objects and radiation, goggles or safety glasses with side shields should be worn even when other eye or face protection is worn.
DON'T weld near cleaning tanks containing chlorinated solvents - the heat breaks down the vapours into very toxic gases.
Laser cutting requires protection from accidental eye contact with the beam or beam reflections.
Properly mount cylinders.
Use correct cylinder regulators.
Ensure adequate lighting.
Ensure proper earthing of arc - welding equipment.
Wear appropriate eye protection during slag removal (chipping).
Avoid radiation exposure from weld check equipment.
Use welding screens to prevent welding flash from affecting others.