## Slide 1: Hazardous Chemicals in the Workplace

## Slide 2: Hazardous Chemical Register
SDS Expired Outside of 5 years

## Slide 3: Control Processes For Chemicals in the Workplace Mineral Turpentine
Usage Workshop Cleaning Product
Ramsol Disinfectant Spray
Usage Office Cleaning Product

## Slide 4: Mineral Turpentine
Licences/Permits: 20L Not Required on Site, SDS and Hazardous Risk assessment to be completed and kept on site. Risk Assessment to be Tool boxed with Staff
Worker Exposure
8hr Day – 5 to 10mins
5 Day Week – 20 to 30 Mins
Workers to Wear safety shoes, overalls, gloves, safety glasses, & respirator when cleaning down work benches

## Slide 5: Mineral Turpentine
Handling and Storage
Handling: Avoid eye contact and skin contact. Avoid inhalation of vapour, mist or aerosols.
Storage: Store in a cool, dry, well-ventilated place and out of direct sunlight. Store away from foodstuffs. Store away from incompatible materials described in Section 10. Store away from sources of heat and/or ignition. Store locked up. Keep container standing upright. Keep containers closed when not in use - check regularly for leaks.
Disposal Precautionary Statement: Dispose of contents/container in accordance with local, regional, national and international regulations.
Transport : Road & Rail Transport Classified as Dangerous Goods by the criteria of the “Australian Code for the Transport of Dangerous Goods by Road & Rail" and the "New Zealand NZS5433: Transport of Dangerous Goods on Land"

## Slide 6: Ramsol Disinfectant Spray
Worker Exposure
8hr Day – 5 to 10mins
5 Day Week – 20 to 30 Mins
Workers to gloves, safety glasses
Licences/Permits: Not Required on Site, SDS and Hazardous Risk assessment to be completed and kept on site. Risk Assessment to be Tool boxed with Staff

## Slide 7: Ramsol Disinfectant Spray
Handling and Storage
Precautions for safe handling
Avoid contact with skin and eyes. Keep away from heat, sparks and open flame. Provide adequate ventilation. Avoid inhalation of vapors. Use approved respirator if air contamination is above an acceptable level. Container must be kept tightly closed when not in use. Use explosion proof electric equipment. Avoid discharge into drains or watercourses or onto the ground.
Storage precautions Keep away from heat, sparks and open flame. Keep container tightly closed. Keep only in the original container
Disposal methods Dispose of waste to licensed waste disposal site in accordance with the requirements of the local Waste Disposal Authority. Pressurized container: Do not empty into drains. Empty containers must not be punctured or incinerated because of the risk of an explosion
Transport hazard class(es) Must not be exposed to temperatures above 50°C

## Slide 8: Safe Systems of Work Supervisors are responsible for ensuring that: Workers and contractors under their control are aware and comply with the hazardous substance requirements in this procedure; A risk assessment is conducted on each hazardous substances prior to use; A worker who may be exposed to a hazardous substance is to be given an induction and ongoing training. Training is to include information about the level of risk identified in the risk assessment and which workers who may be exposed to the substance. Workers are to: Follow the procedure for hazardous substances as Outlined in SWMS Read the Safety Data Sheet (SDS) of a hazardous Substance before using any of the substance Use the appropriate PPE when handling substances and Report any concerns they may have with any hazardous substances. It shall be ensured that an SDS is obtained with each new hazardous substance that is purchased. Incident Response Any accident, incident, or near miss, no matter how slight the resulting injury or damage, must be reported to the department worker in charge or employer representative immediately for appropriate action. Where there is a possibility of further harm or damage occurring, work must be stopped until appropriate measures have been put in place.

## Slide 9: Hazardous Substance Register When compiling a hazardous substance register a survey should be conducted on all substances in the workplace. Once all substances are identified, the SDS’s are to be obtained; A copy of all SDS’s should be located with the Hazardous Substance Register; and The register is to be made available to all staff.

## Slide 10: Environmental System
through management and workers, We need to ensure our operations comply with this policy by developing, implementing and maintaining a system based on ISO 14001:2015.
The Environmental Management System will:
Set a clear policy direction for environmental issues and objectives.
Contain measurable objectives and targets;
Establish systems for auditing monitoring and reporting performance.
Identify and promptly resolve any non-conformances and document any necessary procedural changes.

## Slide 11: Incident Reporting
In order to be successful, Our Company must obtain the most accurate information possible as soon as possible after the incident or near miss. The incident may involve Company workers or property, injury to a private citizen, or damage to private property which may occur as a result of normal Company operations and/or equipment.
The reporting of incidents, accidents and near misses must be made according to the current legislation. This includes the time frame, reporting method, and storage of relevant information for the specified time period.

## Slide 12
Email Consultation