## Slide 1: Maintain Equipment for Activities
SISXFAC001

## Slide 2: Developing a successful maintenance plan:
Have all staff involved with equipment maintenance
Develop maintenance plans in consultation with staff / contractors who use the equipment
Develop specific checklists of equipment and facilities
Record and store all inspections and maintenance procedures.

## Slide 3: Correctly maintained equipment achieves:
Ethical practice
Safety
Lower injury rate
More equipment available
  And happier clientele
Decreased legal costs
Lower insurance premiums
Increase revenue

## Slide 4: Equipment Inventories
Knowing what equipment you have
  Inventory number
  Item
  Model number
  Serial number
  Purchase date
  Location of equipment
  Manufacturer
  Supplier

## Slide 5: Maintenance Logs
Records that keep track when and how equipment has been maintained
Aid in the identification of problems areas
Inventory Number | Item | Serial Number | Maintenance Carried out | Signature | Date

## Slide 6: Maintenance
cleaning
lubricating
reinflating
checking for damage
restocking or refilling
repairing
calibration
storing

## Slide 7: Cleaning fitness equipment
necessary to prevent diseases
  methicillin-resistant Staphylococcus aureus (MRSA)
routinely wipe down exercise equipment after use
disinfect the equipment on a regular basis
  Spray a commercial-grade disinfectant on the surface of the gym equipment
check for any other maintenance that may be needed

## Slide 8: Maintaining strength equipment
UPHOLSTERY
  Check for small tears and rips daily
  Light soiling
    Wipe down with recommended cleaning products or a mild solution of 10% household liquid dish soap and 90% warm water.
  Moderately difficult stains
    Dampen a soft white cloth with a solution of 10% household bleach (sodium hypochlorite) and 90% water. Rub gently.
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx
Notes: 1. UPHOLSTERY
Check for small tears and rips daily a. Light soiling Wipe down soiled upholstery with recommended cleaning products or a mild solution of 10% household liquid dish soap and 90% warm water. For areas requiring something a bit stronger, use a solution of liquid cleanser and warm water applied with a soft bristle brush. Be sure when finished to follow up by wiping away any residual cleaning solution with a water dampened cloth. b. Moderately difficult stains Dampen a soft white cloth with a solution of 10% household bleach (sodium hypochlorite) and 90% water. Rub gently. Again when finished be sure to rinse with a water dampened cloth to remove any residual bleach concentrate. The same procedure can be used with full strength household bleach - if necessary but you must be very careful to rinse this off well to remove any residual bleach. c. Severe stains Allow the bleach to puddle on the affected area or apply with a soaked white cloth for approximately 30 minutes. Rinse with a water dampened cloth to remove any residual bleach. - or as an alternative - Dampen a soft white cloth with rubbing alcohol and rub gently. Rinse with a water dampened cloth to remove any residual rubbing alcohol. d. Upholstery – Luster To restore some of the lost sheen and luster to your upholstery try applying a light coat of spray furniture wax to the upholstery surface. Apply for 30 seconds or so and follow with a light buffing using a clean white cloth
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx

## Slide 9: Maintaining Strength Equipment
UPHOLSTERY
  Severe stains
    Allow the bleach to puddle on the affected area or apply with a soaked white cloth for approximately 30 minutes. Rinse with a water dampened cloth to remove any residual bleach
  Luster
    Apply a light coat of spray furniture wax to the upholstery surface.
    Apply for 30 seconds
    Follow with a light buffing using a clean white cloth
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx
Notes: 1. UPHOLSTERY
Check for small tears and rips daily a. Light soiling Wipe down soiled upholstery with recommended cleaning products or a mild solution of 10% household liquid dish soap and 90% warm water. For areas requiring something a bit stronger, use a solution of liquid cleanser and warm water applied with a soft bristle brush. Be sure when finished to follow up by wiping away any residual cleaning solution with a water dampened cloth. b. Moderately difficult stains Dampen a soft white cloth with a solution of 10% household bleach (sodium hypochlorite) and 90% water. Rub gently. Again when finished be sure to rinse with a water dampened cloth to remove any residual bleach concentrate. The same procedure can be used with full strength household bleach - if necessary but you must be very careful to rinse this off well to remove any residual bleach. c. Severe stains Allow the bleach to puddle on the affected area or apply with a soaked white cloth for approximately 30 minutes. Rinse with a water dampened cloth to remove any residual bleach. - or as an alternative - Dampen a soft white cloth with rubbing alcohol and rub gently. Rinse with a water dampened cloth to remove any residual rubbing alcohol. d. Upholstery – Luster To restore some of the lost sheen and luster to your upholstery try applying a light coat of spray furniture wax to the upholstery surface. Apply for 30 seconds or so and follow with a light buffing using a clean white cloth
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx

## Slide 10: Maintaining Strength Equipment
FRAMES: Rust, Scratches & Gouges
  Perspiration salts are highly corrosive
  Very important to keep the equipment clean and dry to prevent rust and corrosion.
  Wipe up any liquid spills immediately
  Wipe the equipment after each workout
  Remove remaining perspiration from the handrails and painted areas.
  Club staff should clean the equipment at least once a week.
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx
Notes: 2. FRAMES
Rust, Scratches and Gouges Perspiration salts are highly corrosive and will leach into any microscopic openings in even the most impenetrable paint finishes. So it is very important to keep the equipment clean and dry to prevent rust and corrosion. All users should be instructed to wipe up any liquid spills immediately and wipe the equipment after each workout, to remove remaining perspiration from the handrails and painted areas. Club staff should clean the equipment at least once a week. Wipe down with to clean perspiration and dirt off the frame and painted surfaces. To clean perspiration and dirt off the frame and painted surfaces, wipe these areas down Be sure to dry the frames thoroughly. AVOID cleaners containing abrasives - as these could scratch or damage the equipment finish. Although scratches and gouges can and will occur from time to time, addressing them while they are small and manageable will help prevent them from spreading and causing much larger problems in the future. To Minimize Fine or Hairline Scratches: Mild automotive polish applied and removed with a soft, clean cloth will help fill in minor scratches. As perspiration can be insidious in getting into small nooks and crannies in the paint finish a good protective measure would be to apply a light coat of automotive wax to the metal frame parts as an additional protective layer against moisture. Addressing any signs of paint damage or rusting when and if they first appear will greatly increase the longevity of your strength equipment and keep it looking in top shape! As a side note - Do not place the strength equipment in an area of high humidity, such as in the vicinity of a steam room, sauna, indoor pool or outdoors. Exposure to extensive water vapor, chlorine and/or bromine can adversely affect the finish of the product.

## Slide 11: Maintaining Strength Equipment
FRAMES: Rust, Scratches & Gouges
  Addressing any signs of paint damage or rusting when and if they first appear
    Will greatly increase the longevity of your strength equipment
  Do not place the strength equipment in an area of high humidity, such as in the vicinity of a steam room, sauna, indoor pool or outdoors.
    Exposure to extensive water vapour, chlorine and/or bromine can adversely affect the finish of the product.
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx
Notes: 2. FRAMES
Rust, Scratches and Gouges Perspiration salts are highly corrosive and will leach into any microscopic openings in even the most impenetrable paint finishes. So it is very important to keep the equipment clean and dry to prevent rust and corrosion. All users should be instructed to wipe up any liquid spills immediately and wipe the equipment after each workout, to remove remaining perspiration from the handrails and painted areas. Club staff should clean the equipment at least once a week. Wipe down with to clean perspiration and dirt off the frame and painted surfaces. To clean perspiration and dirt off the frame and painted surfaces, wipe these areas down Be sure to dry the frames thoroughly. AVOID cleaners containing abrasives - as these could scratch or damage the equipment finish. Although scratches and gouges can and will occur from time to time, addressing them while they are small and manageable will help prevent them from spreading and causing much larger problems in the future. To Minimize Fine or Hairline Scratches: Mild automotive polish applied and removed with a soft, clean cloth will help fill in minor scratches. As perspiration can be insidious in getting into small nooks and crannies in the paint finish a good protective measure would be to apply a light coat of automotive wax to the metal frame parts as an additional protective layer against moisture. Addressing any signs of paint damage or rusting when and if they first appear will greatly increase the longevity of your strength equipment and keep it looking in top shape! As a side note - Do not place the strength equipment in an area of high humidity, such as in the vicinity of a steam room, sauna, indoor pool or outdoors. Exposure to extensive water vapor, chlorine and/or bromine can adversely affect the finish of the product.

## Slide 12: Maintaining strength equipment
hardware
  Inspect all nuts and bolts for looseness, tighten as required.
GRIPS
  Inspect grips for wear or damage and replace as necessary.
  Inspect all handles and bars for wear or damage
  Inspect all snap links for proper latching or wear
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx

## Slide 13: Maintaining strength equipment
WEIGHT STACKS COMPONENTS & GUIDE RODS
  Inspect all weight stacks and increment weight systems for proper alignment and smoothness of operation.
  Wipe all guide rods clean over their entire length
    lubricate with a light coat of medium weight automotive engine oil.
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx

## Slide 14: Maintaining strength equipment
BELTS
  Replace all belts - at least - once a year.
  Inspect all belts for proper tension and any non-uniformity, wear or damage along their entire length.
  Replace a belt if:
    peeling of the belt's skin
    waves or distortions in the belt
    narrowing of any portion of the belt in excess of 1/32" than the rest of the belt
    any crack or splits
    fraying of the belt
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx

## Slide 15: Maintaining strength equipment
CABLES
  Inspect all cables for
    wear or damage and proper tension.
    Inspect all cables for proper tension and any non-uniformity, wear or damage along their entire length –
      run your fingers on the cable,
      pay particular attention to bends in the cable and attachment points
  Replace all cables - at least - once a year
  Replace worn or damaged cables IMMEDIATELY !
    any tears or cracks in the cables outer sheath that would expose the wire cable
    one or more kinks in the cable
    a curled cable outer sheath
    "necking" a distinct narrowing or stretching of the cable sheath
http://www.cybexintl.com/support/maintenance/techtips/maintainingstrengthequipment.aspx

## Slide 16: Calibrating Treadmill Speed
Measure the length of the belt.
  Tape a piece of string to the treadmill and wind the belt around so that the start of the string does a complete loop.
  Mark and remove the string and measure its length
  Non-string method;
    Move the belt along in short segments and use the ruler to measure each segment and total these for the total length.
Mark the treadmill belt at any point along one edge with chalk (or stick some tape).
Set the treadmill going to a particular speed (based on the speed dial).
Watch the marker come around, and note each time it passes some point.
  When ready, start the stopwatch as the marker passes your view, and time how long it takes to see a set number of revolutions (e.g. 20 loops).
    At higher speeds you may wish to count a higher number of revolutions to get more accuracy.
http://www.topendsports.com/fitness/treadmill-calibration.htm

## Slide 17: Calibrating Treadmill Speed
To determine the treadmill speed (distance / time)
  divide the distance (belt length x number of revolutions) by the time measured.
    Example, if the belt length was 3 meters, and it took 20 seconds for it to do 15 revolutions, then the speed is (3 x 15) / 20 = 2.25 meters/second (or 8.1 km/hr or 5 mph).
Repeat this procedure
  for a range of treadmill speeds
  with someone on the treadmill, to determine if the treadmill calibration still holds true when it is in use.
http://www.topendsports.com/fitness/treadmill-calibration.htm

## Slide 18: Organisational Policies & Procedures
Work Health and Safety (WHS)
storage of equipment
maintenance schedules
record keeping
reporting channels

## Slide 19: Equipment
equipment used within the facility
participant or client-specific equipment
rescue equipment
emergency equipment
large items requiring lifting and assembly

## Slide 20: Equipment
Important to isolate equipment if a fault is found
  Remove the equipment so that it cannot be used
  If not feasible to remove the equipment, put a clearly marked sign on the piece of equipment stating it is “Do Not Use; Out of Order”

## Slide 21: Minor Repairs
replacing faulty or missing parts
repairing component parts
repairing structural fabric

## Slide 22: Safety: Domestic Treadmills
More than 100 serious accidents associated with treadmills have occurred in Australian homes.
Young children are most at risk of injury from treadmills.
  Injuries occur when a child contacts the walking tread while it is in motion, causing serious skin burns and in some cases requiring the child to undergo a skin graft.
  Children have climbed on treadmills in use, causing them to be thrown off. In one case a folded treadmill fell on top of a young child.

## Slide 23: Safety: Domestic Treadmills
To prevent injury
  Use fitness machines in an area that is not accessible to a young child.
  If can’t keep the machine in a child-free area, either place child-proof barriers around the machine or situate it in a position where you can easily see a child approaching you.
  Always keep young children away from fitness machines when they are in use and make sure they can’t reach any moving part.

## Slide 24: Safety: Domestic Treadmills
Understand how to operate the treadmill and learn about the safety functions of the machine.
Consider placing the treadmill in a separate room away from young children. If this is not possible, use safety barriers to keep children away from the machine.
Before using the treadmill ensure children cannot reach or touch the machine.
Keep the area around the treadmill clear of objects.
Wear protective shoes suitable for walking or running when you are using the treadmill.
Keep the treadmill unplugged from power when it is not in use.
When storing the treadmill, especially if it is folded, place it well away from a child’s reach.
Reference: www.accc.gov.au