## Slide 1
LASERS
WORK HEALTH AND SAFETY OFFICER

## Slide 2: Assessment Criteria
Describe the different classes of lasers
What injuries can workers sustain when using lasers?
List work tasks where lasers are involved

## Slide 3: Lasers
Lasers are commonly used for alignment, levelling, control and survey tasks, cutting, welding, marking, scanning and visual effects.

## Slide 4: Legislation
WHS Regulation 2011 s223 – Lasers:
(1) This section applies to the person with management or control, at a workplace, of laser equipment that may create a risk to health and safety.
(2) The person must ensure that laser equipment intended for use on plant is designed, constructed and installed so as to prevent accidental irradiation of any person.
(3) The person must ensure that laser equipment on plant is protected so that any operator of the plant or other person is not exposed to direct radiation, radiation produced by reflection or diffusion or secondary radiation.
(4) The person must ensure that the visual equipment used for the observation or adjustment of laser equipment on plant causes no risk to health or safety from laser rays.
(5) The person must ensure that the workers operating the laser equipment are trained in the proper operation of the equipment.
(6) The person must ensure that Class 3B and Class 4 lasers (within the meaning of AS 2397 Safe Use of Lasers in the Building and Construction Industry) are not used in construction work.

## Slide 5: Classification
AS/NZS IEC 60825.1:2014 – Safety of laser products equipment classification and requirements
Class 1 and 1M - laser products that are safe during use, including long-term direct intrabeam viewing for the naked eye (unaided eye)
Class 1C - laser products that are intended for direct application of laser radiation to the skin or internal body tissues for medical, diagnostic, therapeutic or cosmetic procedures
Class 2 and 2M - laser products emit visible radiation that are safe for momentary exposures but can be hazardous for deliberate staring into the beam.

## Slide 6: Classification
AS/NZS IEC 60825.1:2014 – Safety of laser products equipment classification and requirements
Class 3R (Restricted) - laser products that emit radiation that can exceed the maximum permissible exposure (MPE) under direct intrabeam viewing but the risk of injury in most cases is relatively low. Dazzle, flash-blindness and afterimages may be caused by a beam from a Class 3R laser product in the visible wavelength range, particularly under low ambient light conditions. This may have indirect general safety implications resulting from temporary disturbance of vision or from startle reactions. Such visual disturbances could be of particular concern if experienced while performing safety-critical operations such as working with machines or at height, with high voltages or driving.
Class 3B – laser products that are normally hazardous when intrabeam ocular exposure occurs including accidental short time exposure. Viewing diffuse reflections is normally safe. Class 3B lasers which approach the accessible emission limit (AEL) for Class 3B may produce minor skin injuries or even pose a risk of igniting flammable materials. However, this is only likely if the beam has a small diameter or is focussed.
Class 4 – laser products for which intrabeam viewing and skin exposure is hazardous and for which the viewing of diffuse reflections may be hazardous. These lasers also often represent a fire hazard.

## Slide 7: Instruction, Training and Supervision
Duty holders under the Work Health and Safety (WHS) legislation have an obligation to provide information, instruction, training and supervision to workers using laser equipment to ensure the health and safety of their workers and others. Training should be provided by a competent person, following guidelines provided by the designer, manufacturer or supplier.

## Slide 8: Risk
A laser is a light source that can be dangerous to people exposed to it. Even low power lasers can be hazardous to a person's eyesight. The coherence and low divergence of laser light means that it can be focused by the eye into an extremely small spot on the retina, resulting in localised burning and permanent damage in seconds. Certain wavelengths of laser light can cause cataracts or even boiling of the vitreous humor, the fluid in the eyeball. Infrared and ultraviolet lasers are particularly dangerous, since the body's "blink reflex", which can protect an eye from excessively bright light, works only if the light is visible.

## Slide 9: Managing the risk
Only qualified and trained persons should be assigned to install, adjust and operate the laser equipment.
Use laser protective eyewear
Areas in which these lasers are used should be posted with an appropriate laser warning sign.
Wherever practicable, mechanical or electronic means should be used to assist in the alignment of the laser.
Precautions should be taken to ensure that persons do not look directly into the beam (prolonged intrabeam viewing can be hazardous). Direct viewing of the beam through optical instruments (theodolite, etc.) may also be hazardous.

## Slide 10: Managing the risk
The laser beam should be terminated at the end of its useful beam path and should in all cases be terminated if the hazardous beam path (to Nominal Ocular Hazard Distance) extends beyond the controlled area.
The laser beam path should be located well above or below eye level wherever practicable.
Precautions should be taken to ensure that the laser beam is not inadvertently directed at mirror-like (specular) surfaces (but, more importantly, at flat or concave mirror-like surfaces).
When not in use the laser should be stored in a location where unauthorized personnel cannot gain access.
A Laser Safety Officer (LSO) who is trained in the theory and practical applications of lasers may be appointed for lasers used in high risk applications. (AS2397)